OXNARD FIRE/CUPA

360 W. Second St., Oxnard, CA 93030

TELEPHONE: (805) 385-7722      FAX: (805) 385-8009

GENERAL LABORATORY TESTING REQUIREMENTS AND DETECTION LIMITS FOR PETROLEUM

| GASOLINE |  |
| --- | --- |
| Contaminant |  | Required Method Detection Limit (MDL) |
|  | EPA Analytical Method | Soil (ug/kg) | Water (ug/L) |
| TPHg (total petroleum hydrocarbons as gasoline) (C4-C12) | 8015(M)(8260B) | 100-200 | 50-100 |
| BTEX (benzene, toluene, ethylbenzene & xylenes) MTBE (methyl tertiary butyl ether) DIPE (di-isopropyl ether) ETBE (ethyl tertiary butyl ether) TAME (tertiary amyl methyl ether) TBA (tertiary butyl alcohol) Methanol Ethanol1 | 8260B (8021B) 8260B 8260B 8260B 8260B 8260B 8015(M) 8015(M)(8260B) | 1 2 2 2 2 20 1000 500 | 0.5 1 1 1 1 10 500 250 |
| Total Lead or 6010 | 7420 or 7421 | 1000 | 5 |

| DIESEL |  |
| --- | --- |
| Contaminant |  | Required Method Detection Limit (MDL) |
|  | EPA Analytical Method | Soil (ug/kg) | Water (ug/L) |
| TPHd as diesel (C13-C22) | 8015(M) | 2500-5000 | 500-1000 |
| BTEX | 8260B (8021B) | 1 | 0.5 |

| WASTE OIL |  |
| --- | --- |
| Contaminant |  | Required Method Detection Limit (MDL) |
|  | EPA Analytical Method | Soil (ug/kg) | Water (ug/L) |
| TPH (petroleum fingerprint) Volatile Organics- Full List Total Lead or 6010 | 8015(M) 8260 (B) 7420 or 7421 | 10,000 1000 | 1000 5 |

NOTE:

- Integrate all fuel oxygenate additive concentrations into total petroleum hydrocarbons (TPH) and report it as TPH.

- EPA Method 8021B may be used to substitute EPA Method 8260B only at the sites where no fuel oxygenates have not been previously detected in soil and/or groundwater using EPA Method 8260B.

- All soil samples must be collected in accordance with EPA Method 5035 (except for non-volatile compounds) and a State Certified Laboratory must perform all analyses.

# Footnotes

Methanol and/or Ethanol may have been used historically or currently as a constituent in gasoline, therefore, these compounds must be      included in the first analytical assessment. May be waived by the Project Manager on any subsequent testing.